IFB #15-1049-9RB

Signage, Gateway, County of Henrico

Questions and Answers

October 5, 2015

Q1:	In regards to the “gold colored” border that is shown inset a few inches from the edge. This is a very thin stroke and should be routed into the face of the sign and not raised like the lettering. Should the intent be to route this into the face?

A1:	The border can be routed into the sign.

Q2:	Letters shall be prepped for and covered with 23kt. Gold leaf or approved equal per manufacturer’s instructions. Sign’s shall have letters on the front only, with the appropriate greeting reflected in Attachment D1”

A2:	There is no alternate to gold leaf

Q2a:   On the drawing it shows letters, numbers, the period and the border outline around the edge in a “gold” color. Is the requirement for letters only or is the requirement for all items shown in gold on the drawing to be provided in “23kt. Gold Leaf”?  Also what approved equal (if any) will you accept?

A2a:    All must be in gold leaf

Q3:	Sign structure shall consist of 2 inch by 8 inch aluminum framing structure which is minimum 0.125”. This statement “implies” but does not “require” that the 2x8 should “frame” the sign but that is not clearly indicated and where the framing should be added is also not shown. Confirm how this framing should be added and where?

A3: It should frame the outside of the sign as suggested.

Q4:     At the base of the pole just above the rock base it shows a pole cover/gussets of some type. Is this required?

A4:  Yes

Q5:    Define how this pole is to be provided?

A5: There is to be a break away post to comply with highway safety requirements

Q6:     Is the pole simply two pieces of steel cut in the shape shown (gusset) or is this intended to be completely wrapped around the pole on all sides (cover)?

A6:  The drawing is illustrative only and that gusset would be decorative cover.  Actual design would be reflected in the shop drawings.

Q7:    On the top of the rock base it appears to show some type of cover over the rock base and below the pole cover/gusset. This would often be defined as a type of pre-cast concrete cover over the rock base. This is not called out in the scope of work. What are the County’s expectation for this cover?

A7: Precast concrete

# Text boxes

COMMONWEALTH OF VIRGINIA

COUNTY OF HENRICO

DEPARTMENT OF FINANCE

CECELIA H. STOWE, CPPO, C.P.M.

PURCHASING DIRECTOR

8600 STAPLES MILL ROAD / P O  BOX 90775  / HENRICO  VIRGINIA 23273-0775

(804) 501-5660 FAX (804) 501-5693