The design, construction, and maintenance of stormwater management facilities are governed by the specifications included in Section 9.4 of the Henrico County Environmental Compliance Manual.  The following checklist only identifies the information and details that must be included in the SWM plan.

VA DEQ DESIGN SPEC NO. 3:  GRASS CHANNELS

MINIMUM DESIGN CRITERIA:

- The Grass Channel must meet the following minimum design criteria.  The items checked below have not been properly addressed:

The bottom width must be between 4 and 8 feet.

The channel side slopes must be 3:1 or flatter.

The maximum contributing drainage area to any individual Grass Channel is 5 acres.

The longitudinal slope of the channel must be at least 1% and not greater than 4%.

The maximum flow velocity in the channel must be less than 1ft./s. during a 1-inch storm event.

V10 must be non-erosive.

The channel conveys must contain the 10-year design storm with at least 6 inches of freeboard.

ADDITIONAL COMMENTS:

PLAN REQUIREMENTS:

- Provide a site map identifying pertinent information regarding the Grass Channel.

The contributing drainage area (CDA) boundaries, acreage, and land cover.

Topography of the site area, including the Grass Channel.

The locations of all conveyance system outfalls into the Grass Channel must be shown.

A 16’ wide drainage easement must be provided from all inlets to the outlet(s) if the SWM facility contains public water.

- Provide a plan view showing:

Overall Grass Channel grading

The layout and dimensions of the Grass Channel, including check dams

- Provide profiles, section views, and details that show the following:

Cross-section.

Side slopes

Channel bottom width

Longitudinal slope

Check dam details

10-year storm elevation

- The plans must clearly indicate that the SWM facility has been designed in accordance with Section 9.4.3 (Grass Channels) of the Henrico County Environmental Compliance Manual.

ADDITIONAL COMMENTS:

COMPUTATIONS:

- Hydrologic analysis must be based on a 24-hour storm event using site specific rainfall precipitation frequency data recommended by the U.S. National Oceanic and Atmospheric Administration (NOAA) Atlas 14.

- The U.S. Department of Agriculture’s Natural Resources Conservation Service (NRCS) synthetic 24-hour rainfall distribution and models, including but not limited to TR-55 and TR-20; hydrologic and hydraulic methods developed by the U.S. Army Corps of Engineers;  or other standard hydrologic and hydraulic methods must be to conduct the analyses necessary to demonstrate compliance with the stormwater quality and quantity requirements of Chapter 9 of the Henrico County Environmental Compliance Manual.

- The Rational Method may only be used for evaluating peak discharges such as pipe sizing.

- The Modified Rational Method may only be used for evaluating volumetric flows to stormwater conveyances and may not be used to perform basin routings.

- Provide pre- and post-development hydrologic, hydraulic, and routing information for the 1- year, 2- year, 10- year, and 100-year, 24-hour storms, as needed.

ADDITIONAL COMMENTS:

CHECK DAMS:

- Check dams, if used, must meet the following design criteria:  The items checked blow have not been properly addressed:

Check dams must be composed of permanent, non-erodible material.

Check dams must be firmly anchored into the side slopes and channel bottom.

The maximum check dam height is 18 inches.

Armoring must be provided at the downstream toe of the check dam.

Check dams must be designed with a center weir that is sized to pass the post-development 10-year 24 hour storm event.

The average ponding depth throughout the channel must be between 12 inches and 18 inches.

The ponded water at a downstream check dam cannot touch the toe of the upstream check dam.

Each check dam must have dewatering orifices to minimize standing water.

ADDITIONAL COMMENTS:

LANDSCAPING:

- The construction sequence must specify that a 6” layer of topsoil is required for all areas of the Grass Channel that will be stabilized with a permanent stand of vegetation.  The topsoil layer must be clearly shown on all basin related details to ensure that all post-construction elevations reflect the topsoil application.

- Landscaping of the basin slopes that requires mulching, spraying, etc. must be limited to areas above the elevation of the top of the principal outlet structure elevation and must be done in a manner that does not inhibit maintenance access.

- SWM facilities that are visible from the right-of-way must be effectively screened from the public right-of-way or less intense uses of adjacent properties.  Examples of acceptable screening include fencing, landscaping, or a combination of these features.

ADDITIONAL COMMENTS:

MAINTENANCE:

- A Maintenance Agreement is required, identifying the person or organization responsible for maintenance, authorizing access for inspections and maintenance, and a providing a maintenance inspection checklist.

- Provide a summary of the long term maintenance requirements for the SWM facility on the SWM plan.

ADDITIONAL COMMENTS:

ACCESS:

- All SWM facilities shall be designed to provide the following for adequate access for maintenance activities:

An access area at least 20 feet in width must be provided to the SWM facility from a public road.

An access area 20 feet in width must be provided around the SWM facility that encompasses the highest continuous contour within the SWM facility, embankment, principal spillway outlet, emergency spillway and exit channel.

The access areas must either be in common area or located completely on an individual lot.

The access areas cannot contain any obstacles, or vegetation that would prevent access of maintenance equipment.

The access areas shall not exceed a grade or cross-slope of 12:1.

The access area to the SWM facility must be constructed of load bearing materials.

The access area must provide sufficient turn-around area.

- The access areas identified above must be in an easement that provides access to the County for SWM facilities located in single-family residential developments.

ADDITIONAL COMMENTS:

LOCATION:

- SWM facilities cannot be located within the public right-of-way limits.

- SWM facilities cannot be located within the 100’ RPA buffer or the SPA buffer unless an exception has been granted.

- The SWM facility must be located as follows:

The highest continuous contour on the inside of the SWM facility must be located at least 25’ from the ultimate right-of-way limits for non-residential projects.

The highest continuous contour on the inside of the SWM facility must be located outside of the front yard setback in residential development.

The highest continuous contour on the inside of the SWM facility must be located at least 25’ from the ultimate right-of-way in the side yard in residential development.

There must be a distance equivalent to the rear yard setback between the rear of the buildable area and the highest continuous contour within the SWM facility for all facilities located in the rear lots of residential development.

The SWM facility must be located outside of all transitional or proffered buffer areas or planting strip easements.

SWM facilities must be located outside of the 25-year floodplain.

The SWM facility must be located to the rear of all residential units or in common area that is controlled and maintained by a Homeowners Association.

The highest continuous contour on the inside of the SWM facility must be located at least 20’ from the principal structures in residential development where the proposed SWM facility is located to the side of the principal structure.

ADDITIONAL COMMENTS:

CONSTRUCTION:

- The sequence of construction must address the SWM facility installation and appropriate inspections, including:  initial site preparation, excavation/grading, and installation of the embankment, principal outlet structure, and emergency spillway.  We recommend the County staff be involved in these inspections.

- The sequence of construction must clearly state that a construction record drawing and certification that the stormwater management facility has been constructed in accordance with the approved plan must be submitted to the County and approved prior to Environmental Compliance Bond (ECB) release.

ADDITIONAL COMMENTS:

Reviewed by:

Date Reviewed:

Phone Number:

July 2014